## Slide 1
SLIDE 01 / 03 · PROBLEM STATEMENT
802.1X VLAN Assignment
Silently Fails in Production
AP: AH-AP3000 (00:E6:0E:55:66:80) · Switch: EN_5320 (VOSS/FabricEngine) · Auth: EAP-PEAP/MSCHAPv2 via NPS · 2026-08-07
EXPECTED BEHAVIOUR
✓ User authenticates via 802.1X
✓ NPS returns RADIUS Accept + VLAN 5 attrs
✓ EP1 classifies user → Staff policy
✓ AP tags eth0 uplink: 802.1Q VLAN 5
✓ Client gets DHCP on Staff VLAN 5
ACTUAL BEHAVIOUR
✓ User authenticates via 802.1X
✓ RADIUS Accept arrives
✓ AP tags eth0 with VLAN 5 (proven by pcap)
✗ Switch drops tagged VLAN 5 frames
✗ Client gets NO DHCP Offer — stuck
OBSERVED FALLBACK
When EP1 classification does not fire:
· Frames go out untagged
· Client falls to native VLAN 1
· DHCP succeeds on VLAN 1 (10.153.4.x)
· Staff user silently on wrong VLAN
FAILURE CHAIN:
Wireless
Client ↔ AP
→
AP Uplink
eth0 VLAN-tags
→
Switch Port
Drops VLAN 5 ✗
→
VOSS Fabric
Never reached
Two Compounding Issues
Issue A (Switch): EN_5320 AP uplink port not configured to carry VLAN 5 as tagged — root cause proven by pcap. Issue B (NPS): RADIUS attributes malformed — wrong Tunnel-Type/Medium-Type, multiple Tunnel-Private-Group-Id values.

## Slide 2
SLIDE 02 / 03 · HYPOTHESIS & TEST DESIGN
Designing a Controlled Experiment
KHURSHEED KHAN — VERBATIM HYPOTHESIS (2026-08-07)
"The likely cause of the problem is untagged VLANs on the Fabric_Switch_Port."
DECODING THE EP1 CLASSIFICATION METHODS
"Radius → in EP1 I tag the Radius_Attribute. TVG → In EP1 I tag the third of the three attributes returning from NPS (5). Radius does not work… I know it. But TVG does."
THE FALSIFIABILITY TEST — VERBATIM
"TVG → 5, then have the user get dhcp through VLAN1_default, then 'try to push it onto VLAN5'. So, if you see .1Q with VLAN5 uplink on eth0 from AP, then my hypothesis holds true, EP1 rightsly configures AP with policy but Fabric_Switch cannot take tagged_VLAN5 and is therefore dropping."
EP1 METHOD: RADIUS (BROKEN)
EP1 rule matches on RADIUS Attribute (Filter-Id / Tunnel-* directly from NPS)
→ Does NOT fire. NPS attributes malformed. No VLAN tag applied on eth0.
→ Frames go out untagged. Client falls to VLAN 1 native.
EP1 METHOD: TVG — TUNNEL-PRIVATE-GROUP-ID (WORKS)
EP1 rule matches on Tunnel-Private-Group-Id (attr 81) value = 5
→ FIRES correctly. AP tags eth0 with 802.1Q VLAN per policy.
→ Proven by pcap: 169 tagged VLAN 5 frames in VLAN5_No_DHCP capture.
PREDICTION (IF HYPOTHESIS TRUE)
TVG fires → AP tags VLAN 5 → Discovers sent tagged → zero Offers → switch drops
RESULT AFTER TEST ✓ CONFIRMED
169 VLAN 5 tagged frames on eth0. 22 DHCP Discovers. Zero Offers. Hypothesis holds.
CONTROL RESULT
VLAN1 pcap: zero tagged frames. DHCP Offer at frame 383. Uplink itself is healthy.

## Slide 3
SLIDE 03 / 03 · EVIDENCE
Five Captures — One Verdict
All from AP eth0 (00:E6:0E:55:66:80) · 2026-08-07 18:31–18:58 UTC · Frame counts from binary pcap parse
#
Filename (eth0)
EP1 Method
Frames
Tagged
VLAN on Wire
DHCP Offers
Verdict
1
VLAN5_No_DHCP
TVG5
841
169
VLAN 5
0 Offers
Switch drops
2
VLAN1
None (baseline)
5,227
0
Untagged
Success ✓
VLAN 1 works
3
Radius5_VLAN6
Radius Attribute
41,303
0
Untagged
Success (VLAN 1)
Rule never fired
4
TVG5_VLAN6
TVG5 → VLAN 6
735
114
VLAN 6
0 Offers
Switch drops
5
TVG5_VLAN1-Staff
TVG5 Staff
38,439
0
Untagged
Success (VLAN 1)
Tag push failed
⛔ Root Cause Confirmed
Files 1 & 4: TVG fires, EP1 configures AP correctly, AP tags eth0. Switch receives tagged frames — no DHCP Offer. EN_5320 port drops VLAN 5 & 6 silently.
✅ Fix: Single Action on EN_5320
Add VLAN 5 (Staff) as tagged on the AP uplink port. EP1 → AP → RADIUS chain is working. Only the VOSS switch port config is broken.
⚠️ Secondary Fix: NPS Attributes
Tunnel-Type → VLAN(13), Tunnel-Medium-Type → 802(6), single Tunnel-Private-Group-Id. Fix before retiring TVG workaround.
VERDICT: Hypothesis CONFIRMED — EN_5320 AP uplink port silently drops 802.1Q tagged frames for VLAN 5 and VLAN 6 — Add VLAN 5 to trunk allowed list to resolve

## Slide 4
APPENDIX A · SMOKING GUN — TAGGED VLAN 5, ZERO DHCP OFFERS
File: eth0_VLAN5_No_DHCP.pcap
2026-08-07-183112UTC · 841 frames · 88.5s · TVG5 rule active · 169 tagged VLAN 5 · 0 DHCP Offers
Frame
VLAN Tag
Src IP
Dst IP
Protocol
Info
7
untagged
10.153.4.6
10.152.0.11
RADIUS
Access-Request (EAP-PEAP)
9
untagged
10.152.0.11
10.153.4.6
RADIUS
Access-Challenge
13
untagged
10.152.0.11
10.153.4.6
RADIUS
Access-Challenge
…
untagged
—
—
RADIUS
EAP handshake continues (RADIUS mgmt always untagged — expected)
76
VLAN 5 ◄
0.0.0.0
255.255.255.255
DHCP
Discover — NO OFFER RETURNED (switch drops tagged frame)
96
VLAN 5 ◄
0.0.0.0
255.255.255.255
DHCP
Discover — NO OFFER RETURNED
121
VLAN 5 ◄
0.0.0.0
255.255.255.255
DHCP
Discover — NO OFFER RETURNED
173
VLAN 5 ◄
0.0.0.0
255.255.255.255
DHCP
Discover — NO OFFER RETURNED
282
VLAN 5 ◄
0.0.0.0
255.255.255.255
DHCP
Discover — NO OFFER RETURNED
…
VLAN 5 ◄
0.0.0.0
255.255.255.255
DHCP
22 total Discovers · yiaddr=0.0.0.0 on every frame · client never gets IP
STUDENT ANNOTATION
(1) RADIUS handshake (frames 7–~50) is always untagged — AP management traffic rides native VLAN. This is CORRECT and expected.
(2) From frame 76 onwards, DHCP frames are tagged VLAN 5 — proving EP1 successfully pushed the VLAN 5 policy to the AP after auth.
(3) Every DHCP frame has yiaddr = 0.0.0.0 — meaning only client Discovers/Requests are present. NOT A SINGLE DHCP OFFER in 88 seconds.
(4) Wireshark filter to reproduce: vlan.id == 5 then dhcp — you will see unanswered Discovers only.

## Slide 5
APPENDIX B · CONTROL — UNTAGGED WORKS / TAGGED FAILS
eth0_VLAN1.pcap vs eth0_TVG5_VLAN6.pcap
Same AP · Same 27-minute window · Controls isolate the variable: the 802.1Q tag
CONTROL: VLAN1 — UNTAGGED, BOTH CLIENTS GET IPS
Frame
VLAN Tag
Src IP
Protocol
Info
1
untagged
10.153.4.6
RADIUS
Access-Request
181
untagged
10.153.4.6
RADIUS
Code-4 (→ Accept sequence)
206
untagged
0.0.0.0
DHCP
Discover (iPhone)
383
untagged
10.153.4.6
DHCP
Offer ✓ → iPhone gets 10.153.4.11
858
untagged
0.0.0.0
DHCP
Discover (MacBook)
1128
untagged
10.153.4.6
DHCP
Offer ✓ → MacBook gets 10.153.4.7
Control read: No 802.1Q tag on any frame. DHCP Offers arrive at frames 383 and 1128. Both clients get IPs on VLAN 1. The AP uplink, cable, and switch port are all physically healthy — the failure is exclusively triggered by the VLAN tag.
VLAN 6 REPEAT: SAME FAILURE MODE AS VLAN 5
Frame
VLAN Tag
Src IP
Protocol
Info
31
untagged
10.153.4.6
RADIUS
Access-Request
32–64
untagged
—
RADIUS
EAP-PEAP challenge/response
91
VLAN 6 ◄
0.0.0.0
DHCP
Discover — NO OFFER (switch drops VLAN 6)
103
VLAN 6 ◄
0.0.0.0
DHCP
Discover — NO OFFER
142
VLAN 6 ◄
0.0.0.0
DHCP
Discover — NO OFFER
…
VLAN 6 ◄
0.0.0.0
DHCP
21 total Discovers · 0 Offers · client never gets IP
Why this matters: Switch port rejects ALL tagged VLANs, not just VLAN 5. VLAN 6 test (different EP1 policy, same TVG attribute) produces identical failure. Trunk allowed list is empty or access-mode only.

## Slide 6
APPENDIX C · STUDENT REFERENCE — WIRESHARK DIAGNOSTIC FRAMEWORK
How to Read Any 802.1X VLAN Failure
WIRESHARK FILTERS — CHEAT SHEET
vlan
Show all 802.1Q tagged frames
vlan.id == 5
Isolate VLAN 5 traffic only
dhcp
All DHCP messages
dhcp && vlan
DHCP on a tagged VLAN
bootp.option.dhcp == 2
DHCP Offers only
bootp.option.dhcp == 1
DHCP Discovers only
radius
RADIUS authentication
!vlan && dhcp
DHCP on untagged/native
WHAT EACH FILE PROVES
VLAN5_No_DHCP
EP1→AP signaling works; switch is the break
VLAN1
AP uplink + cable + DHCP server healthy
Radius5_VLAN6
RADIUS Attribute EP1 method is broken
TVG5_VLAN6
Switch drops ALL tagged VLANs, not just VLAN 5
TVG5_VLAN1-Staff
Staff identity confirmed; VLAN enforcement fails
PATTERN: SWITCH DROPS
Tagged DHCP Discovers present. yiaddr = 0.0.0.0 on every frame. Zero Offers in entire capture. Client retries indefinitely.
PATTERN: WORKING
Zero tagged frames. Discover → Offer visible. yiaddr returns non-zero IP. Client associated + routed.
PATTERN: RULE NOT FIRING
RADIUS Accept visible. Zero tagged frames post-auth. Client falls to VLAN 1. No error shown anywhere.
DECISION TREE — ANY 802.1X VLAN FAILURE
1. Open eth0 pcap. Filter: vlan
No frames after auth →
EP1/AP never got VLAN attr.
Check EP1 rule + NPS attrs.
Frames present → step 2
2. Filter: dhcp && vlan
Discovers but no Offers →
AP tagging correctly.
SWITCH PORT is the problem.
Check trunk allowed VLANs.
3. Filter: bootp.option.dhcp==2
Wrong subnet → DHCP/VLAN mismatch.
Right subnet → success.
📌 KEY LESSON
Wireshark on the AP uplink (eth0) is the most powerful diagnostic tool for 802.1X VLAN assignment failures. It sits exactly at the boundary between the wireless/EP1 domain (what the AP was told to do) and the wired/switch domain (whether the switch accepted it). A tagged Discover with no Offer is unambiguous: the AP did its job — the switch did not.